## Slide 1
ECE 1710: Power Distribution Engineering and Smart Grids
Lecture 10
Dr. Robert Kerestes
University of Pittsburgh
Swanson School of Engineering
Department of Electrical and Computer Engineering
Notes: Instructions for editing school and department titles:
Select from menu: View > Master > Slide Master
Click on each text area you wish to edit. Text will become editable.

## Slide 2: Outline
Module #1: Exact line segment model
Module #2: Calculations for line models
Module #3: Line calculation example
Outline of Lecture No. 10

## Slide 3
Learning Objectives:
  Determine generalized line constant matrices
  Solve for line voltages and currents using line constant matrices and source/load conditions
  Solve for voltage unbalance and determine whether it falls within NEMA standards for induction machine operation
  Solve for voltage drops three-wire delta connected distribution lines
  Solve for ground current in three-phase distribution lines
Learning Objectives

## Slide 4: Exact line segment model

## Slide 5: Exact line segment model
Now that we’ve produced line models, the question is what can we do with them?
Can properly calculate voltage drop down a line segment
Can model conductor heat due to current
Can determine if cables are overloaded due to their ampacity constraints

## Slide 6: Exact line segment model
The model of a three-phase, two-phase, or single-phase overhead or underground line is shown in below

## Slide 7: Exact line segment model
For the line segment shown above, the equations relating the input (node n) voltages and currents to the output (node m) voltages and currents are developed as follows. Kirchhoff’s Current Law applied at node m:

## Slide 8: Exact line segment model
In condensed form the line current equation is

## Slide 9: Exact line segment model
Kirchhoff’s Voltage Law applied to the model gives:

## Slide 10: Exact line segment model
The voltage line to ground voltage equation in condensed form is

## Slide 11: Exact line segment model
Substituting the line current into the voltage equation we have
Collecting terms
where

## Slide 12: Exact line segment model
We which we can rewrite as
where:

## Slide 13: Exact line segment model
We can perform a similar derivation (see textbook) to derive
where:

## Slide 14: Exact line segment model
And in partitioned matrix form we have:

## Slide 15: Exact line segment model
We can also solve this for voltages and currents at node m, in terms of voltages and currents in terms of node n by inverting and pre-multiplying
Because
is the inverse of

## Slide 16: Exact line segment model
We can also solve this for voltages and currents at node m, in terms of voltages and currents in terms of node n by inverting and pre-multiplying
Because
is the inverse of

## Slide 17: Exact line segment model
Sometimes it is necessary to compute the voltages at node m as a function of the voltages at node n and the currents entering node m. Solving for the voltage at node m.

## Slide 18: Exact line segment model
Which we can rewrite as
where

## Slide 19
Calculations for Line Models

## Slide 20: Calculations for Line Models
It is often that line-to-line voltages are of interest. These are the difference of line-to-ground voltages:
where
Line-to-line voltage

## Slide 21
Because the mutual coupling between phases on the line segments is not equal, there will be different values of voltage drop on each of the three phases.
As a result the voltages on a distribution feeder become unbalanced even when the loads are balanced.
A common method of describing the degree of unbalance is to use the National Electrical Manufactures Association (NEMA) definition of voltage unbalance:
Voltage Unbalance

## Slide 22: Calculations for Line Models
It is important to know that NEMA standards require that induction motors be derated when the voltage unbalance exceeds 1.0%.

## Slide 23: Calculations for Line Models
For delta connected lines voltage drops must be written in terms of line-to-line voltages because line-to-neutral (line-to-ground) does not exist:
where:
Equivalent line-to-neutral voltage

## Slide 24: Calculations for Line Models
Looking at phase a-b:
But:

## Slide 25: Calculations for Line Models
Substituting:
or:

## Slide 26: Calculations for Line Models
In general, this can be broken into terms of “equivalent” line-to-neutral voltages.
So it is possible to work with these equivalent line-to-neutral voltages for delta connected lines. This is identical to wye circuit calculations.

## Slide 27: Calculations for Line Models
The Kron reduction method was used to reduce the primitive impedance matrix to the 3 × 3 phase impedance matrix. The figure below shows a three-phase line with grounded neutral that is used in the Kron reduction.
Neutral and ground currents

## Slide 28: Calculations for Line Models
In the development of the Kron reduction method, we defined the “neutral transform matrix” [tn].
This matrix is used to calculate the currents flowing through the neutral wire(s)

## Slide 29: Calculations for Line Models
We can then use KCL to calculate the currents flowing into the ground

## Slide 30: Line calculation example

## Slide 31: Line Calculation Example
Example: A balanced three-phase load of 6000 kVA, 12.47 kV, 0.9 lagging power factor is being served at node m of a 10,000 ft three-phase line segment. The load voltages are rated and balanced 12.47 kV. The configuration and conductors of the line segment are those on the next slide
Determine the generalized line constant matrices [a], [b], [c], [d], [A], and [B].
Using the generalized matrices determine the line-to-ground voltages and line currents at the source end (node n) of the line segment.
Determine the voltage unbalance for this system.

## Slide 32: Line Calculation Example
Phase conductors:
336,400 26/7 ACSR
Neutral conductor:
4/0 6/1 ACSR

## Slide 33: Line Calculation Example
zabc =
0.4571 + j1.0791 0.1556 + j0.5027 0.1531 + j0.3860
0.1556 + j0.5027 0.4663 + j1.0492 0.1576 + j0.4247
0.1531 + j0.3860 0.1576 + j0.4247 0.4611 + j1.0661
First calculate the phase impedance matrix:
Ω/mi
Then we must find the lumped parameter impedance, by multiplying this matrix by 10,000/5280

## Slide 34: Line Calculation Example
Zabc =
0.8658 + j2.0438 0.2947 + j0.9521 0.2900 + j0.7310
0.2947 + j0.9521 0.8831 + j1.9871 0.2986 + j0.8043
0.2900 + j0.7310 0.2986 + j0.8043 0.8733 + j2.0192
The lumped parameter phase impedance matrix:
Ω

## Slide 35: Line Calculation Example
yabc =
0.0000 + j5.6711 0.0000 - j1.8362 0.0000 - j0.7033
0.0000 - j1.8362 0.0000 + j5.9774 0.0000 – j1.1690
0.0000 - j0.7033 0.0000 - j1.1690 0.0000 + j5.3910
Next calculate the phase shunt admittance matrix:
μS/mi

## Slide 36: Line Calculation Example
Yabc =
0.0000 + j10.7408 0.0000 - j3.4777 0.0000 - j1.3321
0.0000 - j3.4777 0.0000 + j11.3208 0.0000 - j2.2140
0.0000 - j1.3321 0.0000 - j2.2140 0.0000 + j10.2103
The lumped parameter phase admittance matrix:
μS

## Slide 37: Line Calculation Example
Next finding the generalized line constant matrices [a], [b], [c], [d], [A], and [B]

## Slide 38: Line Calculation Example
a =
1.0000 + j0.0000 -0.0000 - j0.0000 -0.0000 + j0.0000
-0.0000 - j0.0000 1.0000 + j0.0000 -0.0000 + j0.0000
-0.0000 + j0.0000 -0.0000 + j0.0000 1.0000 + j0.0000

## Slide 39: Line Calculation Example
b =
0.8658 + j2.0438 0.2947 + j0.9521 0.2900 + j0.7310
0.2947 + j0.9521 0.8831 + j1.9871 0.2986 + j0.8043
0.2900 + j0.7310 0.2986 + j0.8043 0.8733 + j2.0192

## Slide 40: Line Calculation Example
c =
-0.0000 + j0.1074 0.0000 - j0.0348 0.0000 - j0.0133
0.0000 - j0.0348 -0.0000 + j0.1132 0.0000 - j0.0221
0.0000 - j0.0133 0.0000 - j0.0221 -0.0000 + j0.1021
X 10-4

## Slide 41: Line Calculation Example
d =
1.0000 + j0.0000 -0.0000 - j0.0000 -0.0000 + j0.0000
-0.0000 - j0.0000 1.0000 + j0.0000 -0.0000 + j0.0000
-0.0000 + j0.0000 -0.0000 + j0.0000 1.0000 + j0.0000

## Slide 42: Line Calculation Example
A =
1.0000 + j0.0000 -0.0000 - j0.0000 -0.0000 + j0.0000
-0.0000 - j0.0000 1.0000 + j0.0000 -0.0000 + j0.0000
-0.0000 + j0.0000 -0.0000 + j0.0000 1.0000 + j0.0000

## Slide 43: Line Calculation Example
B =
0.8658 + j2.0438 0.2947 + j0.9521 0.2900 + j0.7311
0.2947 + j0.9521 0.8831 + j1.9871 0.2986 + j0.8043
0.2900 + j0.7311 0.2986 + j0.8043 0.8733 + j2.0192

## Slide 44: Line Calculation Example
Calculating load voltage and current based off of ratings.
Voltage ratings are given in line-to-line, we need to convert to line-to-neutral
kV
The because this is balanced all three phases are equal and separated by 120 degrees so
kV

## Slide 45: Line Calculation Example
Using the ratings for three-phase lagging loads, we can use the following formula to calculate line currents
A
The because this is balanced all three phases are equal and separated by 120 degrees so
A

## Slide 46: Line Calculation Example
Now using the following equation we can calculate the voltage and current at node n using:

## Slide 47: Line Calculation Example
Source line to neutral voltages:
abs(Vlg_n)
ans =
1.0e+03 *
7.5387
7.4513
7.4851
angle(Vlg_n)*180/pi
ans =
1.5730
-118.3011
121.9320

## Slide 48: Line Calculation Example
To calculate the line to line voltages we use:

## Slide 49: Line Calculation Example
Source line to line voltages:
abs(Vll_n)
ans =
1.0e+04 *
1.2974
1.2920
1.3034
angle(Vll_n)*180/pi
ans =
31.4426
-88.1093
151.8697

## Slide 50: Line Calculation Example
Source line currents:
abs(In)
ans =
277.7393
277.7554
277.7601
angle(In)*180/pi
ans =
-25.8253
-145.8221
94.1748

## Slide 51: Line Calculation Example
Now using the following equation we can calculate the voltage unbalance using:

## Slide 52: Line Calculation Example
Now finding the voltage unbalance for the source
dV =
46.9888
40.4035
6.5853
Vunbalance =
0.006272